## Slide 1
Tongue interfaces don’t need to be near the mouth; we can sense tongue movements from the upper face too.
Tongue Gestures for Hands-free Interaction
in Head Worn Displays
Tan Gemicioglu, Mike Winters, Yu-Te Wang, Ivan Tashev
Institution Logo
QR code
Figure placeholder
Eight tongue gestures selected based on design criteria
Our Tongue Interface
Designing Tongue Gestures
By combining the HP G2 Reverb Omnicept Edition VR headset with the Muse 2 EEG headband, we obtained a multimodal sensing system including:
Eye Tracking
Two IMUs and VR position tracking
PPG (heart rate and variability)
EEG (5 channels)
Mouth Camera
Contact
Tan Gemicioglu
tgemici@gatech.edu
@tangemicioglu
Domain | Design Factor | Question
Usability | Accessibility | Which muscles are necessary? With how much force?
 | Privacy | Is the gesture silent? Is it visible visually?
 | Feedback | Does the gesture provide haptic feedback for itself?
 | Simplicity | Is the gesture simple enough to memorize? Can it be performed regularly and quickly?
Recognizability | Signal strength | Is the signal strong enough to separate from noise?
Recognizability | Distinguishability | Is the gesture distinct from other gestures?
 | Rarity | Does the gesture occur naturally in daily activity?
Why Tongue Interaction?
Flowchart of data pipeline from headsets to recognition
Benefits of tongue interaction
Hands-Free
Accessible
Private
Hands-Free
Vs. Speech Recognition: Preserves privacy and usable in a wider range of environments
Vs. Gaze Tracking: Less attention demanding, potentially faster than gaze and dwell
Accessible
For a wide range of movement disabilities
For people whose hands are occupied in warehouses, manufacturing and surgeries
Private
Silent and voice-free, usable in spaces that are loud or where speech is inappropriate
Contained within mouth, giving few visual cues
HP Reverb G2 Omnicept Edition
Muse 2
Our interface
Single Tap
Bite
Shake
Double Tap
Curl Back
Mouth Floor
Left Cheek
Right Cheek

## Slide 2
HP Reverb G2 Omnicept Edition
Muse 2
TongueTap